## Slide 1
DIGITAL CASH REGISTER

## Slide 2
Product Detection
(Sensor)
Price Detection
(Memory)
Accumulation
(1st Counter)
Storage
(2nd Counter)
Work Pyramid
Display
(7 Segment BCD)

## Slide 3
Max Power Consumption=
12 Watts

## Slide 4
Sensor

## Slide 5: IR RECEIVER & TRANSMITTER

## Slide 6
Opening or thin paper
Hard Paper
Card of
specific product
Circuit of
IR receiver and transmitter

## Slide 7
Memory

## Slide 8
IC 74150

## Slide 9
Output
from Comparators
LM 324
Bits of Selectors are shorted
Prices are set as MUX gets supply

## Slide 10
Adder 7483
Shift-register
74194
Binary to decimal conversion seemed Troublesome

## Slide 11
Then…..
another Idea crossed our minds………..
A tricky One!!!

## Slide 12
IC 74190
IC 74191
4-Bit binary Up/Down Counter
4-Bit bcd Up/Down Counter
Output of MUX
goes into COUNTER circuit

## Slide 13
Price in binary

## Slide 14
Price in binary
Reset Cash Register
load/count

## Slide 15
Reset Cash Register
load/count

## Slide 16
Reset Cash Register
load/count

## Slide 18
Component name | Quantity | Cost (BDT)
12V Adapter | 1 | 150
IC 7805 | 1 | 15
Heat sink | 1 | 30
LM324 | 2 | 30
IR emitter | 4 | 10
IR receiver | 4 | 10
IC 74150 | 4 | 320
555 timer IC | 1 | 30
IC 74191 | 1 | 30
IC 74190 | 2 | 60
Cost of circuit component

## Slide 19
Component name | Quantity | Cost (BDT)
IC 7432 | 1 | 20
IC 7404 | 1 | 20
Switches | 3 | 30
Resistors | 30 | 10
Potentiometer | 2 | 20
Wire |  | 60
IC 7447 | 2 | 60
7seg display | 2 | 20
Leds | 5 | 15
Breadboard | 5 | 900
Total |  | 1840

## Slide 20
For 4 bit price system, Total No. of ICs = 15
99 is the highest we can count
Increasing 2 more, we can have 5 bit price system
Increasing 4 more and 1 display, We can count 999